## Slide 1: Plastic sampling
How bycatch became a hot topic
Margriet Schoor (Rijkswaterstaat),
Frank Collas, Stephanie Oswald (Radboud University)
March 4, 2021
Rws informatie

## Slide 2: The Waal stow net fishery
More plastic than fish!
A lot of plant material
Collecting the plastic every 1 to 2 hours
Rws informatie

## Slide 3: Plastic pollution in rivers
Rws informatie
Rivers transport plastic to the sea
Multiple sources and sinks
Research mainly focussed on:
  River banks (Schone Rivieren)
  Top of water column
Stow net fishing? (Eelschokker/Ankerkuil)
Assesment of plastics in the entire water column
Van Emmerik & Schwarz 2019

## Slide 4: Research questions
What plastic materials are present in the water column?
What is the origin of the plastic?
How much plastic is potentially transported yearly?
Goal of this pilot
to learn about the main sources of plastic
to come to a monitoring strategy (method, variation in density, costs)
Rws informatie

## Slide 5: Method
Cleaned and sieved
Meso plastics (0,5 – 2,5 cm) and Macro plastics (>2,5 cm)
Identification according to river OSPAR categories
Counted
Partly weighed
Statistics: Bootstrapping to derive yearly numbers of plastics
Rws informatie

## Slide 6: Collected plastic categories
Rws informatie
Plastic foil
Candy packages
Cord & string <1cm diameter
Tampon packages
Sanitary wipes
marco
meso

## Slide 7: Collected cord & string
Rws informatie

## Slide 8: Variation amount of collected plastic categories
Sept > Okt
2019 > 2020  Corona effect?
Rws informatie
Macro
Meso
Collas et al in prep.

## Slide 9: Country of origin
18 countries
Majority from:
  Drainage area Rhine
  Eastern European countries
Shipping?
USA - Toerism?  river cruises
Rws informatie

## Slide 10: Density of plastic
Macro plastics: 0 à 18 items / 1000 m3 average: 5 items/1000 m3
Meso plastics: about the same
But: underestimation due to the stow net
Concentration higher than other Western European rivers (Ems, Weser, Elbe; Schöneich-Argent et al. 2020)
  ~0.02 items/1000m3 versus ~10 items/1000 m3 (Waal)
Rws informatie
Macro
Meso
Collas et al in prep.

## Slide 11: Yearly numbers of plastic in Rhine water
Based on low discharges! (<1800 m3/s)
And tested net efficiency
Rws informatie
Waal
Collas et al in prep.
Waal: 300 million pieces/year (=79% QLobith during sampling)
Boven Rijn: 380 million pieces/year

## Slide 12: Mass of plastic
no clear relation between the number of pieces and the mass of a sample
Large variation, low density of large/heavy pieces pieces
Chart: Macroplasics >2,5 cm
| 56 | 107 | 110 | 83 | 75 | 160 | 82 | 86 | 97 | 40 | 135 | 147 | 155 | 104 | 105 | 103 | 120 | 56 | 60 | 49 | 44 | 92 | 90 | 75 | 91 | 51 | 33 | 88 | 80 | 87 | 92 | 107 | 106
LTD | 35.1201 | 42.4341 | 37.4361 | 56.0652 | 49.1711 | 130.8183 | 33.8931 | 93.4881 | 92.4863 | 95.2671 | 58.9181 | 22.5671 | 80.0991 | 51.7961 | 35.7751 | 51.8692 | 27.5631 | 24.6071 | 30.1021 | 17.7361 | 7.4251 | 163.6911 | 63.2202 | 23.533 | 21.1521 | 13.7841 | 22.0551 | 40.0721 | 86.4711 | 30.6041 | 38.1682 | 62.7701
Hoofdgeul | 44.9003 | 81.2673 | 30.7741 | 47.4981 | 12.9101 | 81.4441 | 11.6171 | 7.6421 | 167.3521 | 4.4961 | 9.4021 | 3.6591 | 9.7251 | 4.7891 | 17.1371 | 8.4311 | 13.8711 | 3.4001 | 29.8911 | 16.9071 | 8.5261 | 25.2611 | 47.0191 | 3.1401
Chart: Mesoplastics 5-25 mm
| 32 | 33 | 40 | 30 | 25 | 58 | 60 | 36 | 31 | 26 | 27 | 93 | 45 | 76 | 70 | 34 | 75 | 27 | 17 | 15 | 11 | 27 | 25 | 24 | 38 | 14 | 15 | 46 | 41 | 50 | 27 | 30 | 28
Oevergeul | 0.4701 | 2.9981 | 1.2871 | 1.6101 | 1.6101 | 2.2531 | 2.5771 | 0.6121 | 6.6512 | 4.0361 | 0.5601 | 0.7441 | 1.5531 | 1.1311 | 1.4141 | 0.4391 | 1.4851 | 1.4831 | 0.7661 | 0.9721 | 0.7021 | 1.4651 | 1.0151 | 1.0301 | 1.8371 | 0.8901 | 2.0041 | 1.7791 | 0.712 | 2.2091 | 1.6461 | 1.8041 | 0.578
Hoofdgeul | 1.8331 | 1.192 | 1.23 | 2.5711 | 1.3631 | 1.6611 | 1.6541 | 1.1881 | 1.2221 | 1.1941 | 2.279 | 0.134 | 1.0961 | 1.0621 | 1.1051 | 1.026 | 0.652 | 0.33 | 1.5421 | 0.611 | 1.1401 | 0.131 | 0.065 | 1.0871
Rws informatie
data 2019
data 2019

## Slide 13: Mass plastic in main channel and side channel
compared with main channel:  more plastic in side channel
Meso (5-25 mm)
Significant (1%)
Macro (>2,5 cm)
significant (1%)
Niet significant
significant (5%)
Rws informatie
 Mass 
data 2019

## Slide 14: What is going on ?
Plastic sampling met 3 (larvae) nets above each other (ATKB):
  Test with net 0,5 cm
  Plastic sampled during flood
  Plastic sampled in Tolkamer and IJssel
Analysis by Radboud University:
  Samples ankerkuil 2020
  Samples larvae nets
GPS trackers to follow plastic 2 weeks
Larvae nets catch 2,5 times more meso plastic
Macro plastic density comparable, but low numbers
Rws informatie
1 m

## Slide 15: Next april plastic campaign:
Different methods & different places:
2 weeks ankerkuil Waal (GBRA)
  Collecting plastics from stow net
  Collecting plastics from larvae nets
  Collecting plastics from a new fine net (3m x 1 m, 3 mm mash)
  ADCP measurement of flow velocity
  Test of DIDSON sonar camera
Collecting plastic with larvae net on Niederrhein (GBRA)
6 days Boven Rijn (RWS - not sure yet)
  Collecting plastics from larvae net
  Collecting plastics from a new fine net
River banks plastic collecting (WUR - not sure yet)
Rws informatie

## Slide 16: Future wishes plastic research GBRA
More plastic sampling (depth, width, longitudinal, seasonal variability)
  to come to a monitoring strategy
  focus on in/output at borders
Collaboration with RU and WUR and Germany
Identify main sources (e.g. tributaries, shipping) and put on the agenda
Rws informatie